## Slide 1: Curriculum and Course Design for Mechatronics and Robotics Engineering Education ASEE Workshop Sunday, June 26, 2022 Minneapolis, Minnesota
Carlotta A. Berry, PhD
Professor
Lawrence J. Giacoletto Endowed Chair In
Electrical and Computer Engineering
ROSE-HULMAN INSTITUTE OF TECHNOLOGY
Notes: Schedule
  Introduction (10 minutes) – Introduce the workshop origins, goals, and mission.
  Session I (45 minutes) Mechatronics & Robotics Engineering Curricula
  Motivation, goals, objectives, and outcomes
  Core courses, electives, capstone projects
  Break (10 minutes)
  Session II (45 minutes) Introduction to Mechatronics & Robotics Courses
  Course organization and objectives
  Homework / Labs / Projects
  Break (10 minutes)
  Session III (45 minutes) Intermediate & Advanced Mechatronics & Robotics Courses
  Course organization and objectives
  Homework / Labs / Projects
  Capstone design projects
  Summary and Future Directions (15 minutes)
Room: MCC - 205A

## Slide 2: Software Design Plans and Simulators
SDP enable students to develop a systematic approach for robot algorithms
SDP give them options for creating their code including pseudocode, state diagrams, flow charts, and subsumption architecture
Simulators allow students to test out and debug their theories before dealing with odometry error, bandwidth limitations, memory issues, power consumption, and sensor error

## Slide 3: Pseudocode
An algorithm is a procedure for solving a problem in terms of actions to be executed.
Pseudocode is an artificial and informal language that helps programmers develop algorithms.

## Slide 4: Pseudocode Example (Stopwatch)
Initialize counter to 0
Initialize reset to 1
Initialize run to 0
Is the button pressed?
  No, stay in current state, reset
  Yes, increment counter, set reset to zero, set run to 1
Is the button pressed?
  No, stay in current state, run
  Yes, save final counter value, reset still 0, set run to 0
Is the button pressed?
  No, stay in current state, stop
  Yes, return to reset
3 states
Reset
Run
Stop
Notes: Can also be more like a programming language, if statements, etc… do example

## Slide 5: Flowchart Example (Stopwatch)
Start
Counter=0
Reset=1
Run=0
Button
Counter=Counter+1
Reset=0
Run=1
Clear
Run
1
0
1
Button
Counter=Counter
Reset=0
Run=0
Button
0
0
1
State0
State1
Stop
3 states
Reset
Run
Stop

## Slide 6: State Diagram Example (Stopwatch)
Notes: If I was writing code, I would make functions reset, run and stop

## Slide 7: Robot Motions

## Slide 8: Simulate Robot Motions

## Slide 9: Robot Motions
Notes: <object width="560" height="315"><param name="movie" value="//www.youtube.com/v/huQSWZX1Glo?hl=en_US&amp;version=3&amp;rel=0"></param><param name="allowFullScreen" value="true"></param><param name="allowscriptaccess" value="always"></param><embed src="//www.youtube.com/v/huQSWZX1Glo?hl=en_US&amp;version=3&amp;rel=0" type="application/x-shockwave-flash" width="560" height="315" allowscriptaccess="always" allowfullscreen="true"></embed></object>

## Slide 10: Robot Motions

## Slide 11: Simulator for Robot Motion
Go to Dawson virtual robot simulator
  modify code to move forward to collect all coins
  write code to move robot in a s
    square
    Circle
    figure 8
Simulator link:
bit.ly/dawsonSim1

## Slide 12: Wall Following Subsumption Architecture
Add
Follow Left & Follow Right

## Slide 13: Wall Following Simulation

## Slide 14: Wall Following with Bang-Bang Control

## Slide 15: Robot Simulator for Wall Following
Go to Dawson virtual robot simulator
  modify code to drive robot to follow wall
  modify code to drive robot to follow wall and collect all coins
  modify code to follow wall and collect coins robot using bang-bang control
  modify code to follow wall and collect coins robot using proportional control
  modify code to follow wall and collect coins robot using PD control
Simulator link:
bit.ly/dawsonSim2